## Slide 1: Ka-band beamforming IC for LEO user terminals
Design review · SiGe BiCMOS 130 nm
L. Boccia, E. Arnieri, G. Amendola · ESA project meeting · Rende, 3 September 2026

## Slide 2: Architecture
01
System partitioning between silicon and antenna

## Slide 3: Design objectives
Four-channel Tx/Rx beamformer, 27.5–31 GHz
6-bit phase and 5-bit gain control per channel
Integrated LNA with NF < 3 dB across band
Antenna-in-package co-design with 2×2 sub-array
Tape-out planned Q4 2026 (MPW run)

## Slide 4: Silicon vs. antenna: split of responsibilities
RFIC / MMIC
Beamforming core, phase shifters, VGA
Front-end LNA / PA
SPI control and calibration registers
Antenna & package
Stacked-patch elements, dual polarisation
Flip-chip interconnect and thermal path
Array-level calibration strategy

## Slide 5: Chip micrograph and layout
Die size 3.8 × 3.0 mm²
Four identical channels with shared LO distribution
Digital core in the centre to minimise routing
Inserire immagine
(micrografia, layout, foto banco)
Fig. 1 — Beamformer IC, SiGe BiCMOS 130 nm

## Slide 6: Measured performance
< 3 dB
Noise figure
Rx mode, 27.5–31 GHz
360°
Phase range
6-bit, RMS error < 4°
+14 dBm
Output P1dB
per channel, Tx mode
1.2 W
DC power
4 channels, Tx

## Slide 7: Gain vs. frequency — four channels
Chart: Frequency (GHz)
| 26 | 27 | 28 | 29 | 30 | 31 | 32
CH1 | 14.8 | 16.6 | 17.6 | 18 | 17.6 | 16.6 | 14.8
CH2 | 15.2 | 17 | 18 | 18.4 | 18 | 17 | 15.2
CH3 | 14.5 | 16.3 | 17.3 | 17.7 | 17.3 | 16.3 | 14.5
CH4 | 15 | 16.8 | 17.8 | 18.2 | 17.8 | 16.8 | 15

## Slide 8: Thank you — questions?